## Slide 1
SNMP
CONCEPTS & EVOLUTION
Presented by Team B

## Slide 2
SNMP CONCEPTS & EVOLUTION
  Definition: SNMP is a protocol used for managing devices on IP n/w (e.g., routers, switches,).
  Manager-Agent Model: SNMP operates with a manage that communicates with agents to manage and monitor network devices.
  Management Information Base (MIB): A hierarchical database of network device information, where each item is assigned a unique Object Identifier (OID).
  Basic Operations: The manager sends requests like GET (retrieve data) and SET (modify data), while the agent responds or sends unsolicited TRAPs (alerts).

## Slide 3
SNMP EVOLUTION
SNMPv1 (1988):
  First version of SNMP.
  Basic functionality for monitoring and managing network devices.
  Lacks security (no encryption or authentication).
SNMPv2 (1993):
  Introduced improvements like bulk data retrieval (GETBULK) for more efficient data collection.
  Better error handling and performance.
  Limited security enhancements, still inadequate for sensitive networks.
SNMPv3 (1998):
  Added strong security features, including encryption and authentication.
  Focused on user-based security (USM) and view-based access control (VACM).
  Fully backward-compatible with SNMPv1 and SNMPv2.

## Slide 4
SNMP ARCHITECTURE
  The Simple Network Management Protocol (SNMP) architecture includes four layers.
The SNMP architecture includes the following layers:
  SNMP Network Managers
  Master agents
  Subagents
  Managed components

## Slide 5
  SNMP Network Manager:
    Software that requests and displays data from master agents. It allows selection of items to monitor and how to display them.
  Master Agent:
    Interface between the SNMP Network Manager and subagents.
  Subagent:
    Software that provides data to the master agent.
  Managed Component:
    Hardware or software (e.g., routers, servers) that provides a subagent for monitoring.
.

## Slide 6
  Managed Component:
    Devices or software (like servers, routers, or printers) that send data through a subagent.
  Management Information Base (MIB):
    Lists of data that a subagent shares with the master agent, using SNMP rules.

## Slide 7
SNMP QUERY
  SNMP Queries are interactions between the manager and the agent. The manager sends requests, and the agent responds with information.
Query Types:
  GET: Retrieves a specific variable from an agent.
  GETNEXT: Retrieves the next variable in the MIB tree.
  GETBULK: Efficient retrieval of large data sets (supported in SNMPv2 and later).
  SET: Modifies a variable in the agent’s MIB.

## Slide 8
SNMP COMMANDS
Basic Commands:
  GET: Requests the value of a specific object.
  SET: Modifies the value of a specific object.
  GETNEXT: Retrieves the next object in sequence.
  GETBULK: Fetches multiple data points efficiently.
  TRAP: Asynchronous notification from the agent to the manager (e.g., when something goes wrong).
  INFORM: Similar to TRAP but expects an acknowledgment.

## Slide 9
SNMP TRAPS
TRAPS:
  Definition: An unsolicited message from an agent to the manager to alert about critical events.
  Use Case: Alert for system failures, high CPU usage, interface down, etc.
Types:
    ColdStart: The device has rebooted.
    LinkDown: Network interface went down.
    AuthenticationFailure: An invalid community string was used in an SNMP request.

## Slide 10
YANG EVOLUTION & BACKGROUND
  YANG: A language for setting up and monitoring network devices.
  Background: Created by IETF to improve on SNMP for more complex networks. Often used with NETCONF and RESTCONF.
  Advantages:
    Clear data definitions.
    Handles both configuration and status info.
    Works across different vendors, using a model-driven approach.

## Slide 11
SNMP LIMITATION
  Key Limitations:
    Security: Early versions (SNMPv1, v2) lacked encryption and strong authentication.
    Scalability & Overhead: Inefficient for large networks and frequent polling strains resources.
    Limited Write Capabilities: Primarily read-focused with fragmented vendor MIB implementations.

## Slide 12
OPERATORS' REQUIREMENT
Modern Network Management Needs:
  Enhanced Security: Strong encryption and authentication are needed, improved in SNMPv3 but still limited.
  Real-time Alerts: Immediate insights are essential, like SNMP TRAPs or newer methods with YANG/NETCONF.
  Automation: Automated configuration and policy management are crucial, where SNMP falls short but YANG excels.
  Interoperability: Need for vendor-neutral management across various devices.